## Slide 1: Introduction to SDN
Portions of this PPT draw from PPT authored by Professor Dijiang Huang at
Arizona State University

## Slide 2: Outline
Concept of SDN
OpenFlow – a SDN Implementation

## Slide 3: What is SDN?
Software-Defined Networking, a.k.a. the programmable network
A new network architecture
A new network operating system
A Generalized network virtualization
(more…)

## Slide 4: Why do we need SDN?
Do you think a Network system simple?
Networks used to be simple: Ethernet, IP, TCP….
New control requirements led to great complexity
  Isolation  VLANs, ACLs
  Traffic engineering  MPLS, ECMP,Weights
  Packet processing  Firewalls, NATs, middleboxes
  Payload analysis  Deep packet inspection (DPI)
  …..
Mechanisms designed and deployed independently
  Complicated “control plane” design, primitive functionality
Notes: ECMP: Eqaul Cost Multi-Path routing strategy.

## Slide 5: Networking Devices
Packet Processing
Operating System
App
App
Forwarding
Switching
Interface Virtualization
Control and Management APIs
Routing
Access Control
Traffic Engineering
Management
Network Router
Protocol and operation model

## Slide 6: A Typical Network

## Slide 7: Today’s Distributed Networking Systems
Close Boxes, Fully Distributed Protocols
Closed Operating Environment
Packet Processing
Operating System
App
App
Packet Processing
Operating System
App
App
Packet Processing
Operating System
App
App
Packet Processing
Operating System
App
App
Packet Processing
Operating System
App
App
Traffic control decisions are mostly made locally, i.e., usually require a negotiation procedures among network entities (e.g., routing).
Not easy for testing and experiments, i.e., usually requires a separate testing environments.
Routing
Access Control
Traffic Engineering
Management
Interface Virtualization
Control and Management APIs
Forwarding
Switching

## Slide 8: Data processing and Control in Distributed Systems
Packet Processing
Operating System
App
App
Packet Processing
Operating System
App
App
Packet Processing
Operating System
App
App
Packet Processing
Operating System
App
App
Packet Processing
Operating System
App
App
Data processing and controls are not separated. Algorithms, e.g., routing, is performed in a distributed environment. Each router acts individually, much likes our current social networks.
Packets

## Slide 9: Switched Networks in OpenStack
Switches learn from the network traffic they observe and decide independently.

## Slide 10: Traditional network node: Switch
Two “planes”
  Control Plane: computing the forwarding state
    Involves coordination with rest of system
  Data Plane: forwarding packets
    Based on local forwarding state

## Slide 11: Two “planes”
Two fundamental terms to begin understanding the SDN
Processing Plane | Where it runs | How fast these processes run | Type of processes performed
Control Plane | Switch CPU (smart but slow) | In the order of thousands of packets per second | Routing protocols (i.e. OSPF, IS-IS, BGP), Spanning Tree, SYSLOG, AAA (Authentication Authorization Accounting), NDE (Netflow Data Export), CLI (Command Line interface), SNMP
Data Plane | Dedicated Hardware ASIC (fast but dumb) | Millions or Billions of packets per second | Layer 2 switching, Layer 3 (IPv4 ¦ IPv6) switching, MPLS forwarding, VRF Forwarding, QOS (Quality of Service) Marking, Classification, Policing, Netflow flow collection, Security Access Control Lists
Notes: ASIC: application-specific integrated circuit.
MPLS: Multiprotocol Label Switching
VRF: Virtual Routing and Forwarding

## Slide 12: Traditional network node: Router
Router can be partitioned into control and data plane
  Management plane/ configuration
  Control plane / Decision: OSPF (Open Shortest Path First)
  Data plane / Forwarding
Adjacent Router
Router
Management/Policy plane
Configuration / CLI / GUI
Static routes
Control plane
OSPF
Neighbor table
Link state database
IP routing table
Forwarding table
Data plane
Data plane
Control plane
OSPF
Adjacent Router
Data plane
Control plane
OSPF
Routing
Switching

## Slide 13: SDN definitions
SDN is an approach to building computer networks that separates and abstracts elements of these systems – from Wikipedia
  In SDN, not all processing happens inside the same device.
In the Software Defined Networking architecture, the control and data planes are decoupled, network intelligence and state are logically centralized, and the underlying network infrastructure is abstracted from the applications. – from ONF White Paper

## Slide 14: How to do it?
How to get a simpler, more systematic design for the so complicate network control mechanisms?
The power of Abstraction
  “Modularity based on abstraction is the way things get done.” – Barbara Liskov
Abstractions  Interfaces  Modularity

## Slide 15: Finding control plane abstractions
Task: Compute forwarding state:
  Consistent with low-level hardware/software
    which might depend on particular vendor
  Based on entire network topology
    because many control decisions depend on topology
  For all routers/switches in network
    every router/switch needs forwarding state

## Slide 16: SDN Abstractions
SDN is defined precisely by three abstractions: Forwarding, Distribution, Configuration
  Abs#1: Be compatible with low-level hardware/software
    Need an abstraction for general forwarding model
  Abs#2: Make decisions based on entire network
    Need an abstraction for distributed network state
  Abs#3: Compute the configuration of each physical device
    Need an abstraction that simplifies configuration
Notes: Why “distributed state”? Because the communication in control programs is ALL directed towards collecting/disseminating/or calculating on distributed state.
Tell you how later, but this is the purpose of the abstractions…

## Slide 17: Abstraction Detail
Abs#1: Forwarding abstraction
  OpenFlow is current proposal for forwarding standard
  Configuration in terms of flow entries: <header, action>
Abs#2: Network state abstraction
  Global network view abstraction
  Network OS (controllers) queries network devices to form “view” and sends commands to them to control forwarding
Abs#3: Specification abstraction
  Abstract view of network: simple model with only enough to specify goals.
  Network virtualization: map abstract configuration to physical configuration

## Slide 18: From traditional networking to SDN
Packet Processing
Operating System
App
App
Packet Processing
Operating System
App
App
Packet Processing
Operating System
App
App
Packet Processing
Operating System
App
App
Packet Processing
Operating System
App
App
Network Operating System
App
App
App
App
Programmability
Virtualization
Networking Resource Isolation
Fine-grained access control
Global view

## Slide 19: Abstract SDN Model
Simple Packet Processing: forwarding
Simple Packet Processing: forwarding
Simple Packet Processing: forwarding
Simple Packet Processing: forwarding
Simple Packet Processing: forwarding
Network Operating System
Network Virtualization
App
App
App
App
Open interface to hardware

## Slide 20: What SDN looks like
Application Tier
Control Plane Tier
Data Plane Tier
(Network OS)

## Slide 21: Clean Separation of Concerns
Control program: express goals on abstract view
  Driven by Operator Requirements
Virtualization Layer: abstract view  global view
  Driven by Specification Abstraction for particular task
NOS: global view  physical switches
  API: driven by Network State Abstraction
  Switch interface: driven by Forwarding Abstraction

## Slide 22: Software-Defined Networking
Data Plane Tier
  Packet forwarding (as per flow table), packet manipulation (as per flow table), statistics collection
Control Plane Tier (Network OS)
  Data plane resource marshaling, common libraries (e.g., topology, host metadata, state abstractions)
Application Tier
  Virtual network overlays, network slicing (delegation), tenant-aware broadcast, application-aware path computation, integration with other software packages, policy, security, traffic engineering.

## Slide 23: How to process the SDN requests?
Write a simple program to configure a simple model
  Configuration merely a way to specify what you want
Examples
  ACLs: who can talk to who
  Isolation: who can hear my broadcasts
  Routing: only specify routing to the degree you care
    Some flows over satellite, others over landline
  TE: specify in terms of quality of service, not routes
Virtualization layer “compiles” these requirements
  Produces suitable configuration of actual network devices
NOS then transmits these settings to physical boxes
Network OS
Global Network View
Abstract Network Model
Control Program
Network Virtualization

## Slide 24: Outline
Concept of SDN
OpenFlow – a SDN Implementation

## Slide 25: OpenFlow
OpenFlow is a Layer 2 communications protocol that gives access to the forwarding plane of a network switch or router over the network.
OpenFlow enables controllers to determine the path of network packets through the network of switches.

## Slide 26: How it works?
The OpenFlow protocol is layered on top of the Transmission Control Protocol (TCP), and prescribes the use of Transport Layer Security (TLS).
Controllers should listen on TCP port 6653 for switches that want to set up a connection. Earlier versions of the OpenFlow protocol unofficially used port 6633.
A
B
A
B
Initial packet of a flow
The subsequent packets of the flow

## Slide 27: OpenFlow Switch, v 1.0
OpenFlow allows remote administration of a layer 3 switch's packet forwarding tables, by adding, modifying and removing packet matching rules and actions.

## Slide 28: OpenFlow Flow Table Abstraction
Controller

## Slide 29: Flow entry examples
Switching
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
00:1f:..
*
*
*
*
*
*
*
port6
Flow Switching
port3
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
00:20..
00:1f..
0800
vlan1
1.2.3.4
5.6.7.8
4
17264
80
port6
Firewall
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
*
*
*
*
22
drop
Routing
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
5.6.7.8
*
*
*
port6
VLAN Switching (Efficient !!!)
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
vlan1
*
*
*
*
*
port6,
port7,
port9
00:1f..

## Slide 30: OpenFlow Header v.1.1

## Slide 31: OpenFlow Switch
OpenFlow-compliant switches come in two types:
  OpenFlow-only: support only OpenFlow operation, in those switches all packets are processed by the OpenFlow pipeline, and can not be processed otherwise.
  OpenFlow-hybrid: support both OpenFlow operation and normal Ethernet switching operation, i.e. traditional L2 Ethernet switching, VLAN isolation, L3 routing (IPv4 routing, IPv6 routing...), ACL and QoS processing.
  The OpenFlow pipeline of every OpenFlow switch contains multiple flow tables, each flow table containing multiple flow entries.

## Slide 32: OpenFlow matching process
ONF, “OpenFlow Swith Specification v.1.3.0”, June, 2012

## Slide 33: Programmability
OpenFlow native programmability
  Redefined the flow format, actions, and etc.
Controller programmability
  Call Openflow provided API to control

## Slide 34: OpenFlow Controllers
Name | Language | Platform(s) | Original Author | Notes
Openflow Reference | C | Linux | Stanford/Nicira | Not designed for extensibility
Nox/Pox | Python, C++ | Linux | Nicira | Actively developed
Beacon | Java | Win, Mac, Linux, Android | David Erickson (standford) | Runtime modular, web UI framework, regression test framework
Trema | Ruby, C | Linux | NEC | Includes emulator, regression test framework
Ryu | Python | Linux | NTT | Supports openstack and openflow 1.3
Floodlight | Java | any | BigSwitch | Support openstack and java based

## Slide 35: SDN Stack
Notes: This is all GENI or other project upon openflow architecture

## Slide 36: Example of OpenFlow Applications

## Slide 37: References
Scott Shenker, Software Defined Networking, http://inst.eecs.berkeley.edu/~ee122/
OpenFlow official website at http://www.openflow.org
NOX controller at http://www.noxrepo.org/
J. Pettit, J. Gross, B. Pfaff, M. Casado, S. Crosby, “Virtual Switching in an Era of Advanced Edges,” 2nd Workshop on Data Center – Converged and Virtual Ethernet Switching (DC-CAVES), ITC 22, Sep. 6, 2010.
B. Pfaff, J. Pettit, T. Koponen, K. Amidon, M. Casado, S. Shenker, “Extending Networking into the Virtualization Layer,” HotNets-VIII, Oct. 22-23, 2009.
S. Zhou, “Virtual Networking,” ACM SIGOPS Operating Systems Review, 2010.
N. Mckeown et al., “OpenFlow: Enabling Innovation in Campus Networks,” white papers. The OpenFlow Switch Consortium, March 2008, http://www.openflowswitch.org//documents/openflow-wp-latest.pdf
Y. Luo et al., “Accelerating OpenFlow Switching with Network Processors,” Proc. ACM/IEEE Symp. Architectures for Networking and Communications Systems (ANCS 09), ACM Press, 2009.
J. Naous et al., “Implementing an OpenFlow Switch on the NetFPGA platform,” Proc. ACM/IEEE Symp. Architectures for Networking and Communications Systems (ANCS 08), ACM Press, 2008.
H. Chen et al., “A Survey on the Application of FPGAs for Network Infrastructure Security,” IEEE Communications Surveys & Tutorials, June 2010.
F. Azmandian et al., “Virtual Machine Monitor-Based Lightweight Intrusion Detection,” ACM SIGOPS Operating Systems Review, July 2011.
H. Bos and K. Huang, “A network intrusion detection system on ixp1200 network processors with support for large rule sets,” in Technical Report 2004-02. Leiden University, 2004.